## Slide 1: ATC Future Comms Technology

## Slide 2: ATC Future Comms
Introduction
Current State of Controller Comms
  Serial
  Networking
ATSC4 Developments
  Network Interface – Full TCPIP Stack
  Modem Interfaces (4G, ADSL, Fibre)
  Amendment 3 Changes

## Slide 3: ATC Future Comms
ATSC4 Developments
  SNMP Support (SolarWinds)
  Site Region Server (SRS) Ready
  Syslog Server Ready
  Blue Tooth Data Collection Ready
  Ethernet - Fibre (NBN) Ready
  RMS Amendment 3 interfaces

## Slide 4: ATC Future Comms
Why discuss comms for controllers?
  Current PSTN network being obsoleted (Dec 17)
Benefits for Road Authorities?
Avoid vendor lock in
Open Standards – support for web browser configuration, file storage etc

## Slide 5: ATC Future Comms
To interface serial comms to SCATS over network the SCATS IP protocol was developed.
Essentially, it allows a legacy comms port to be connected over a IP network.

## Slide 6: ATC Future Comms

## Slide 7: ATC Future Comms
The interface device is pretending to be a networked node
Not an architecturally clean solution – it is simply band-aiding the root problem of the Traffic Signal Controller not having a TCPIP stack implemented.
What happens when RMS Amendment 3 comes into force – this problem gets worse !!

## Slide 8: ATC Future Comms
Road Authorities can implement a fault tolerant network for some or all of its ITS devices.
An Ethernet interface allows Road Authorities to add fault tolerant network routing if needed but not essential (VMWare NSX).
Fault Tolerant Routing is available from any device vendor – it is not a telco bespoke solution!

## Slide 9: ATC Future Comms
The ATSC4 can interface directly to network protocols.
It can implement secure web server, respond to network monitoring tools (Solarwinds, Tivoli).
It can scale up if more data originates from within intersection (C-ITS, Detector Data, New Sensors etc)

## Slide 10: ATC Future Comms
SNMP – the ATSC4 can serve SCATS and Solarwinds at the same time.
The Syslog Server is an open standard used in UNIX systems – it is not a modem specific solution
The ATSC4 provides a RICH set of data STRAIGHT FROM THE CONTROLLER. Not a modem specific set of messages

## Slide 11: ATC Future Comms

## Slide 12: ATC Future Comms

## Slide 13: ATC Future Comms
The ATSC4 can be interfaced to current and emerging networks.
Making ITS devices network native will simplify managing such devices.
Road Authorities can seek partners to implement resilient networks.
Many vendors can implement fault tolerance without vendor lock in.

## Slide 14: ATC Future Comms
By using open standards protocols Road Authorities can leverage networked ITS devices.
Reduced implementation costs.
When NBN is rolled out, ATSC4 will plug directly into Network Interface Device (NID)

## Slide 15: ATC Future Comms
NBN Packet Priority – time sensitive data such as CCTV, telephony, SCATS etc.
NBN Fault Tolerance – multi-WAN
http://www.nbnco.com.au/sell-nbn-services/products-services-pricing/nbn-co-ethernet-bitstream-service.html

## Slide 16: ATC Future Comms
Routers are workhorse of network
Routers handle ATSC4, CCTV, Detectors, VMS, LUMS with or without priority
Redundancy of comms is NOT due to service providers but network design

## Slide 17: ATC Future Comms
Networked ITS Assets will eliminate legacy protocols & devices in time
Wider choice of ITS Products to Road Authorities by adopting open standards protocols
Telecommunications has gone completely IP at the back-end

## Slide 18: ATC Future Comms
ATSC4 Interface Integration Testing
  PSTN Interface – (Dial IP)
  4G Interface
  Bluetooth Interface
  ADSL2
  SHDSL (Future)

## Slide 19: ATC Amend’t 3 Changes
Amendment 3 Changes in a Nutshell
  Network native controller interface – SCATS and Web Interface for maintenance
  Housing encoding for LV, ELV, Phase, Xformer Dimming.
  New Personality Module XPM 48 Way IEC
  Dim-By-Wire Signal & feedback for dimming new LED Lanterns.
  Better lamp fault tolerance handling and reporting.

## Slide 20: ATC Amend’t 3 Changes
Amendment 3 Changes
  2 Network Interfaces (comms (XNS SCATS) and maintenance)
  New Secure web interface to configure controllers (XNW).
  Accommodate USB interface to file storage, transfer, loading (XUP).
  New Personality Module (XPM) with separate READ ONLY and WRITE areas (local config info).

## Slide 21: ATC Amend’t 3 Changes
Amendment 3 Changes
  Personality module can be inserted/removed on live running controller without damage (controller will stop if configured for loss of XPM).
  Local intersection specific data – veh det sensitivity, IP address etc stored in “writeable area of personality).

## Slide 22: ATC Amend’t 3 Changes
Amendment 3 Changes
  PSTN modem interface (XRJ) – line to internal modem (ATSC4 has this).
  Signal Group Voltage suppressing circuits now mandatory – ATSC4 always had them.
  Site ID now provides configuration data for operating voltage & type (LV or ELV etc) – controller housing characteristic.

## Slide 23: ATC Amend’t 3 Changes
Amendment 3 Changes
  16 types of housing are configurable – by setting of diodes in Site ID and connected via ZHC.
  Phase or Amplitude dimming encoded
  LV (240v) and ELV (42v) encoded
  Additional CB for CCTV to be included.
  Flash Change Over relays have a test button and flash suppression capability.
  Generator Input Circuit mandatory

## Slide 24: ATC Amend’t 3 Changes
Amendment 3 Changes
  Dim-By-Wire – two control signals 15v from Site ID to command LED lanterns to dim internally (not dim from the signal group output) via ZDC.
  Single feedback wire for dim-by-wire into controller 8v.
  Front panel indicators Red = Dimmed, Green = Undimmed.

## Slide 25: ATC Amend’t 3 Changes
Amendment 3 Changes
  Ethernet ports to be MDI/MDX compatible – you can use straight or cross over Ethernet cable to ATSC4.
  Secure web browser interface to supervise operation of controller and is the NEW HHT.
  The controller communicates via secure network protocols.

## Slide 26: ATC Amend’t 3 Changes
Amendment 3 Changes
  Better lamp fault monitoring with varying lamp fault tolerance based on signal group loads.
  In dimming mode, the algorithm shall use different lamp fault wattage values to avoid false faults.