## Slide 1: SCATS Update
SNUG, February 2017
Tauranga

## Slide 2: SCATS Update – Feb 2017
SCATS 6.9.3 CR – reported issues
SCATS 6.10 CR
  New features
  VC5.1 trial results
  SCATS Priority Engine (SPE) trial results
Planned work packages
  Vehicle detection technology
  Upstream vehicle detection
  External detectors

## Slide 3: SCATS 6.9.3 CR - Issues
Pedestrian movement terminates on expiration of minimum green interval
  RPS before NXP
Phase gap events not recorded as specified
Rare incorrect VC 5.x recognition
  Communication stalls – set to VC=4!
Patch released 6.9.3 Build 21
If CL > 180 seconds, SK=AR! fails

## Slide 4: SCATS 6.10 CR – prepared
New ITS interface
  System status
  Intersection status/monitor
  Scheduled Dwell replacing GWR
SDS support – TransIS replacement
    SPaT map and message
    SSDI – spatial support for measured data
SPE
  SPE-Web interface
  Spatial queries instead of SCATS centric

## Slide 5: SCATS 6.10 CR - cont’d
SCATS SIM Repeatability
Access: support new operating systems
  Windows 10
  Access uses true-type font
  Unlimited VR
  Increased the number of scheduler items
  Provide SS fallback reason
  Show last 4 voted SP, LP, marriage

## Slide 6: VC5.1 trial
4 x each controller type deployed
True signal group state – verified
Intersection fallback - verified
Issues
  SS fallback is not managed as specified
  Detector state gets stuck on actuation
VC6.2 is now compiled (VC6.1 + VC5.1)

## Slide 7: SPE trial: PTIPS
PTIPS replacement

## Slide 8: SPE trial: TPE extension

## Slide 9: SBC 1: vehicle detection
Re-wiring of existing induction loops
Provide information on travel speeds and vehicle lengths
New detection technology:
  Count on half loop
  Calculate DS with full loop
  Optimise the offset time between intersections

## Slide 10: SBC 2: upstream detection
Measure all arriving vehicles, including queued vehicles, using mid-link upstream detectors
Improve SCATS real-time optimisation at the downstream traffic signals
Combine with SBC1 (detection technology + associated SCATS algorithm changes)
Improve congestion measurement
  slow short vehicle from an efficient, fast long truck

## Slide 11: SBC 3: external detectors
Enable use of IP base detectors
Provide drivers for converting continuous detection to SCATS input (Vo, NonOcc)
Provide interface delivering speed and length of each vehicle/pedestrians
Ability to define SI in a region from external sources